Safety Solutions Ltd

HAZOP GUIDEWORDS

GENERAL

Control System & Equipment Failure

Progress along the line and for every instrument/transmitter/measuring device and equipment item in sequence consider: Fail High, Fail Low, Fail As Is, Fail on Demand

Valve fails/sticks: open/closed

How may an operator (incorrectly) respond to an inaccurate measurement

Heat exchanger leak, which way, when?

Pump trip, electrical/mechanical

Agitator stops/Impeller drops

Filter blocks and /or holes,

HOW WILL THE OPERATOR KNOW?

Human Error

What reliance is placed upon procedure? Is this reasonable?

How often is task performed?

What is consequence of error (wrong set point, incorrect quantity entered)?

Is there an independent back up?

What standard is required from operator (experienced, well motivated, high standard of training or vice versa – does it match reality)?

What is environment for task? (Good surroundings, quiet or noisy & busy)

How long to make decision?

Will operator realistically detect or respond to the deviation?

What is the likelihood (frequency or probability) of error?

Is an engineering solution required?

High Flow

Pump or compressor over-speed Delivery vessel pressure lost Large differential pressure Suction pressurised Heat exchanger failure Valve failure open, not closed Loss of containment

Low Flow

Partially closed valve High downstream pressure Inadequate line size or valve Blockage, hydrate filter, scale Pump or compressor trip, cavitation Loss of feed Loss of containment Control failure

Reverse / Misdirected Flow

Pump failure/high head High downstream failure NRV sticks open Siphon Poor isolation Valves incorrectly lined out Vacuum Shut down for maintenance Valves incorrectly lined out Valve not seated Valve (e.g. 3 way) fails to move (e.g PLC sequence)

High Pressure

Thermal expansion Fire Hammer Pressure surge Chemical reaction Blocked outlet Flooded vessel/column Compressor/Pump over-speed Deadhead Heat exchanger tube failure Fluid density increase Valve failure (open/closed) Weather Control system failure Freezing EDP/ESD valve mis-timing.

Low Pressure

Loss of containment Compressor over-speed Compressor or pump failure Low Temp (e.g. weather) Sudden condensation Blocked vent (on falling level) Decrease in fluid density Passing valve. Leak Instrument failure Failed exchanger tube Failed valve (open/closed) Burst rupture disc

Differential Pressure

Blocked filter/demister/pipeline. High flow Collapsed media Flooded trays or packed bed Foaming Hydrates High Viscosity

High Temperature

Fire Weather Exothermic Reaction Loss of Endothermic Reaction Heat of absorption etc Too high temp on heating fluid Heat tracing Pump dead head Internal recirc Flame impingement Poor compressor efficiency Loss of control Cooling system failure/fouling Loss of power

Low Temperature

Plant EDP Sudden loss of pressure Expanding vapour (JT) Excess pressure drop Flashing liquid Poor heat transfer (fouling) Endothermic reaction Loss of exothermic reaction Excess refrigeration Weather Heat tracing failure Control Failure

High Level

Blocked outlet Valve closed /throttled Foaming Outlet pump failure Sudden loss of pressure High feed flow Control Failure

Low Level

Feed pump loss of efficiency Feed valve partially closed Blockage in feed line. Loss of containment Drain open Control system failure

Composition Change / Impurities

Change in concentration 2-phase flow Supplier error Over/Under reaction Control failure Impurities checks: Gas, Liquid, Solid Supply contamination – How?, With what? What else do they supply? dedicated tanker? What assurance – CoA, Operator checks? Chemical reaction Corrosion products Lube oil Heat exchanger failure Air ingress (vacuum), seal failure Dead legs (bugs) Hydrates Previous batch

Changes Inside Equipment

Inc Corrosion & Erosion

Internal equipment breakage, packing collapse. High/Low Reaction Rate Runaway reaction – (foaming exotherm) Pressure surge Hammer (Liquid Slug or Vapour Condensing) Valve hysteresis Fouled instruments CORROSION/EROSION Cavitation

Plant Items Operable / Maintainable

Do the operators think they have the tools to run the plant? Are all items of equipment accessible by operators (valves, local instruments, transmitters)? Can the plant and individual items be isolated? Can the plant be purged and vented? Can the instruments be tested? HAS A LAYOUT REVIEW TAKEN PLACE INVOLVING THE DESIGN TEAM, OPERATIONS AND MAINTENANCE. IF NOT SCHEDULE AS A HAZOP ACTION. Are all items of equipment accessible by maintenance personnel (valves, instruments, motors)? Are all items of equipment removable e.g agitator shafts, heat exchanger bundles. motors, rotors? Can the plant and individual items be isolated? Can the instruments be tested? Are any items critical, expensive single stream or not readily available (long lead) Spares lists? HAS A LAYOUT REVIEW TAKEN PLACE INVOLVING THE DESIGN TEAM, OPERATIONS AND MAINTENANCE. IF NOT SCHEDULE AS A HAZOP ACTION.

Testing

Provision for pressure testing? Hazardous area electrical inspections planned? Control system requirements e.g calibration Plant performance testing? Sampling

Trips & Relief

Relief: Do changes impact on relief e.g CV trim, or blow down solenoid. Relief: Is relief valve sizing basis documented and known for the review Trips: What is the “consequence of failure on demand” Has a review taken place to determine the SIL level or is one planned? Has the SIL level been achieved?

Static, Earthing, Bonding, Insulation

Has it been provided? Is testing required? Tank filling? Bag filling (solids) Instrument damage?

Hazardous Area Zoning/HSNO

Service Failure

Power Instrument Air Cooling Water Nitrogen Flare system Vent system Communications –loss of Telemetry – loss of

CIP

(Food)

Is the line adequately covered by the CIP system Has adequate backflow protection been provided Are critical items (e.g RO membranes, CS fans) protected Will the line be adequately flushed by the final rinse?

Critical Hygiene

FOOD

Have all points where contamination can occur been identified Has the system been approved by MAF Have any failures which result in recycle/bypassing from /to “pasteurised” product been identified?

Overview

General: Fire detection / protection Emergency response (Fire, ambulance, call points) First-aiders? Emergency showers Security Hazards of materials (MSDS) Noise, dust HSNO requirements – separation, signage, identification, secondary containment, approved handlers, location, stationary tanks, emergency plans? material compatibility Training: operators, maintenance? Service failure overview- Integrity of supply? Lightning protection? Major HAZARDS – fire, explosion, gas release, dust explosion. PPE Communications? Storage & Handling? Effluent ? Construction? Start Up, Shut Down? Performance test? Resource Consent limits known? Product Quality limits known?